## Slide 1: Looking inside Computer I/O Devices
By Liam Osman

## Slide 2: Agenda
USB
  Versions
  Encoding
  Serial vs. Parallel
  Pinout
Digital Input
  Mouse
  Keyboard
Digital Output
  Displays
Analog Audio
  Speakers
  Microphones
Conclusion

## Slide 3: USB

## Slide 4
Multiple Connectors
Multiple Protocols
USB A & C connecters are most used
USB Versions
From https://en.wikipedia.org/wiki/USB

## Slide 5: Binary Signals
Computers can only work in binary numbers, not decimal
The simplest way of implementing this is 1 = high, 0 = low
Voltage is changed to match
101102
= 2^4 + 2^2 + 2^1
= 2210
https://www.geeksforgeeks.org/difference-between-unipolar-polar-and-bipolar-line-coding-schemes/#

## Slide 6: Serial vs. Parallel
Serial
Parallel
https://commons.wikimedia.org/wiki/File:Serial_and_Parallel_Data_Transmission.svg
Uses 1 data line
Cheaper construction
Less crosstalk
No clock skew
Uses many data lines
More data per clock
No processing at beginning and end

## Slide 7: Encoding
Encoding maps every output to a binary code
Descending order of bits
100 0001 = A
110 0001 = a

## Slide 8: USB Pinout (Type A, USB 2.0)

## Slide 9: Differential Pairs
Electromagnetic interactions in nearby environment = noise
Differential pairs allow us to reduce signal noise by subtraction
Source is sent both as positive and negative
(+) – (–) = + for signal
(+) – (+) = 0 for noise
https://handwiki.org/wiki/images/3/3d/Differential_signal_and_common-mode_interference_fed_into_a_differential_amplifier.svg

## Slide 10: Digital Input

## Slide 11: Optical Mouse Sensing
An LED illuminates the floor through a lens (UV light nowadays)
Mouse sensor captures low resolution picture constantly
Each polling tick, mouse looks at picture movement
https://www.researchgate.net/figure/Structure-of-optical-mouse-sensor_fig1_221644902

## Slide 12: Optical Mouse Polling
Hertz = Cycles / Seconds
The faster the update cycles are, the smoother the cursor
Default USB polling is 125Hz = 0.8ms between updates
New USB allows up to 8000Hz!
An example image from a mouse sensor.
https://hackaday.com/2014/01/14/your-mouse-is-a-terrible-webcam/

## Slide 13: A Problem With Keyboards…
A full-size keyboard has more than 100 keys!
Most microcontrollers don’t have so many inputs, and making them with so many is costly, so we need a better solution
We can design the inputs of a keyboard to overlap the same inputs on the keyboard’s microcontroller
This presents a problem we need to solve though…

## Slide 14: Keyboard Ghosting
If a keyboard has too many keys held down, depending on design, it may not register an additional keypress
Try it out! Hold down a bunch of keys and see what happens
This keyboard blocking was created to prevent ghosting
Ghosting is when keys register which you haven’t pressed

## Slide 15: Keyboard Key Sensing
Pressure from key switches forces layers together to conduct
When you press far enough to establish a path, input occurs

## Slide 16: Keyboard Traces
PCB traces connect to make a large matrix of possible inputs
https://www.brunerd.com/blog/2009/08/25/apple-keyboard-a1243-disassembly/

## Slide 17: Keyboard Matrix
Let’s imagine a square 4x4 keyboard with only 16 keys…

## Slide 18: Keyboard Matrix
The controller cycles fast, scanning each column progressively
https://pcbheaven.com/wikipages/How_Key_Matrices_Works/

## Slide 19: Keyboard Matrix
Each column scan is coded to interpret each possible input key
https://pcbheaven.com/wikipages/How_Key_Matrices_Works/

## Slide 20: Keyboard Matrix
In this image B2, B3, and C2 are pressed, but C3 will register!
https://pcbheaven.com/wikipages/How_Key_Matrices_Works/

## Slide 21: Keyboard Matrix
We can fix this design with diodes
Diodes are small and cheap pieces which only let current flow one way
Placing a diode on each switch prevents the backflow of voltage across the circuit causing ghosting
https://pcbheaven.com/wikipages/How_Key_Matrices_Works/

## Slide 22: Digital Output

## Slide 23: Binary to Decimal Conversion
https://www.newvisiondisplay.com/types-of-lcd-technology/
LCD’s are everywhere in our life. One of the most common types is Twisted Nematic (or TN). We’ll see:
What makes it change color?
How do display a binary number?

## Slide 24: Twisted Nematic (TN) Displays
Very Cheap
Liquid Crystal Solution will align to voltage
Default twisted arrangement allows light to pass polarizers
Aligning to the charge blocks it!
https://commons.wikimedia.org/wiki/File:TN-LCD-schematic-MS-208kB.png

## Slide 25: BCD to 7 Segment Display Decoder
4 bits are needed for 0-9
7 segments to display
Decoder must match for EVERY possible option
A truth table shows all possibilities for the code
https://www.geeksforgeeks.org/bcd-to-7-segment-decoder/#

## Slide 26: BCD to 7 Segment Truth Table
https://www.geeksforgeeks.org/bcd-to-7-segment-decoder/#
https://commons.wikimedia.org/wiki/File:7_segment_display_labeled.svg
0123456789

## Slide 27: Pixels and Color
Red, blue, and green subpixels
Each one has brightness level
8 bit RGB gives 16 million colors
HD resolution has 2 million pixels
4K resolution has 8 million pixels
https://commons.wikimedia.org/wiki/File:Pixel_geometry_01_Pengo.jpg

## Slide 28: HDMI Cables
HDMI is a serial protocol, but with some parallel features
Parallel channels for Red, Green, and Blue subpixels
Data channels cycle to also transmit audio and data
https://commons.wikimedia.org/wiki/File:HDMI_Connector_Pins.jpg

## Slide 29: Analog Audio

## Slide 30: Analog Signals
The natural world is made of continuous analog signals
Sound waves are analog in nature, and must be made as such
https://www.monolithicpower.com/en/analog-vs-digital-signal

## Slide 31: Analog to Digital Sampling
We have to sample an analog signal repeatedly to get a value
The frequency of the sampling is the sample rate (usually kHz)
The amount of possible steps we measure is our bit depth
CD’s run at
  44.1 kHz
  16 bit depth
https://neurotext.library.stonybrook.edu/C7/C7_1/C7_1.html

## Slide 32: Usage in Audio
Microphones input analog sound
ADC converts it into a digital file
DAC and filters convert to analog
Your speakers amplify signal and play it as analog sound for you
https://medium.com/@graysparkpune/best-sound-engineering-academy-in-pune-gray-spark-academy-a30d74dac40e

## Slide 33: Conclusion

## Slide 34: Conclusion
We need to represent all our data in binary numbers and codes
Generally, serial communication is used to transfer our data
Mice take pictures and compare them to track your movement
Keyboards need to scan for key presses in a large matrix
LCD displays align with voltage applied to match a color input
HDMI outputs map to a large grid of RGB subpixels on screen
Analog signals must be used for natural waves like sound
Analog mic input is sampled to digital to make a sound file
Sound files are converted to analog waves on speaker to play

## Slide 35: Next Events